## Slide 1: Mechanical Vibration
Dr. Vishisht Bhaiya
Assistant Professor
Department of Civil Engineering
S. V. National Institute of Technology Surat

## Slide 2: Vibration
A mechanical vibration is the motion of a particle or body that oscillates about a position of equilibrium.
A mechanical vibration generally results when a system is displaced from a position of stable equilibrium.
The system tends to return to this position under the action of restoring forces
But the system generally reaches its original position with an acquired velocity that carries it beyond that position.
Because the process can be repeated indefinitely, the system keeps moving back and forth across its position of equilibrium
Notes: Most vibrations in machines and structures are undesirable because of the increased stresses and energy losses that accompany them.
Our present study is limited to the simplest types of vibrations––namely, the vibrations of a body or a system of bodies with one degree of freedom.
The system tends to return to this position under the action of restoring forces (either elastic forces, as in the case of a mass attached to a spring, or gravitational forces, as in the case of a pendulum).

## Slide 3: Terms of Vibration
The time interval required for the system to complete a full cycle of motion is called the period of the vibration.
The number of cycles per unit time is defined as frequency
The maximum displacement of the system from its position of equilibrium is called the amplitude of the vibration.
When the motion is maintained by the restoring forces only, the vibration is said to be a free vibration.
When a periodic force is applied to the system, the resulting motion is described as a forced vibration.
When the effects of friction are neglected, the vibrations are said to be undamped vibration.

## Slide 4: Contd..
When the effects of friction are considered, the vibrations are said to be damped vibration
Single degree freedom of system is a system in which the system is constrained to move in only one direction. Therefore, it requires only one coordinate to specify its position.
Multi degree freedom of system is a system in which the system is free to move in more than one direction.

## Slide 5: Undamped Free Vibration
When the block will be displaced from its equilibrium position, free vibration will start.
k
M
x(t)
M
kx
FBD of mass M

## Slide 6: Undamped Free Vibration
k
M
Equation of simple harmonic motion
From FBD we get,
Acceleration is directly proportional to displacement and is in opposite direction

## Slide 7: Contd…
General solution of the equation is
If A and B are expressed as and
Note that A and B depends on initial condition

## Slide 8: Contd…
Time period =
Maximum Amplitude =
Phase Angle =

## Slide 9: Equation of motion using Energy method
  Draw the FBD of the body after giving a small displacement from its equilibrium position.
  Define the location of the body from its equilibrium position using appropriate position coordinate system.
  Formulate equation of energy i.e K.E. + P.E. = constant
  Take time derivative of energy equation and factor out common terms
  Express the resultant differential equation in the following form
  Use the expressions developed for simple harmonic motion to find other response quantities

## Slide 10: Energy Method
Restoring forces are conservative in nature.
Therefore, conservation of energy equation can be used to obtain natural frequency.
k
M
x
Eqm. position
Total energy of system = K.E. + P.E.
= Constant

## Slide 11: Contd..
Differentiating total energy with respect to time, we get,
Max. K.E. =
Max. P.E. =
k
M
x
Eqm. position

## Slide 12: Undamped Forced Vibration
In undamped forced vibration, a periodic force is present.
k
M
x(t)
M
kx
FBD of mass M

## Slide 13: Undamped Forced Vibration
k
M
From FBD we get,
Second order non homogeneous differential equation
Solution will have two parts
Complementary Solution
Particular Solution

## Slide 14: Complementary Solution
It is determined by putting right hand side equal to zero.
or

## Slide 15: Particular Solution
As the motion is periodic therefore, the solution will also be of periodic form.
Double differentiating we get,
Putting in equation of motion we get,

## Slide 16: Contd…
Hence general solution is
Transient vibration (free vibration) in case of damped vibration will die down, whereas, steady state vibration (forced vibration) will continue .
Transient Vibration
Steady state Vibration

## Slide 17: Contd…
Modification factor (p) is the ratio of steady state amplitude to the maximum static deflection caused by periodic force.
Modification factor vs Forcing frequency
Resonance